## Slide 1
Linux kernel porting to Microcontrollers
A possible embedded-systems frontier

## Slide 2
The Linux Kernel
Linux is a mainstream free open-source kernel with high customization properties.
It is a monolithic kernel, which supports a large number of architectures.
It is most known to be used in servers, computers and some embedded systems.
But it relies on several HW resources and its size grows over development time…

## Slide 3
Aim of the project
The didactictal scope of the project is to replicate the design flow for a soft real-time embedded system, based on Linux (mainline v5.12) on a MMU-less device.
It must also take into account the memory footprint for the minimal OS obtained with the kernel, init and some small executables.
Furthermore, the system will be headless. It will only support a connection using a usart as a tty serial port to send kernel and programs info to a pc and eventually get input from it.

## Slide 4
Aim of the project
Note: the project is still under development.
The whole project can be found on GitHub.
Bootloader source: https://github.com/LucaLombardini/afboot-stm32
Kernel source: https://github.com/LucaLombardini/stm32f401re_lnx_5.12
Project source:
https://github.com/LucaLombardini/full_embedding_linux

## Slide 5
Target Architecture
The chosen target is the microcontroller STM32F401RE, which is a commercial and easy to retrieve uC.
It is a Cortex-M4 based MCU (32-bit CPU), with a base clock frequency of 84MHz, 512kB of Flash memory and 96kB of static RAM.
This MCU does not support an external interfacing BUS for memory chips.

## Slide 6
Target Architecture
The project should then be demonstrated by means of the NUCLEO-F401RE development board, which is also easily available.
The board has also the HW facility to translate usart to USB, which is useful in this context.

## Slide 7
System Layout
The system layout consist of considerations over the whole memory space, regarding which part goes where.
Considering the general structure of a computing system and how an OS works, the ROM memory must contain:
- the bootloader
- the kernel
- a filesystem
Note: the last one contains the codes to be executed for the init process and all the other processes (supervised by the kernel environment), together with the files needed for their execution.

## Slide 8
System Layout
+------------+
| | FLASH_START_ADDRESS
| bootloader |
| |
+------------+
| | FLASH_START_ADDRESS + size(bootloader)
| deviceTree |
| |
+------------+
| | FLASH_START_ADDRESS + size(bootloader)
| kernel | + size(DTB)
| |
+------------+
| | FLASH_START_ADDRESS + size(bootldr)
| filesystem | + size(DTB) + size(kernel)
| |
+------------+
So, the FLASH organization is planned to be as shown:
Note: the labels indicates the starting address for that Flash section.

## Slide 9
System Layout
+------------+
| | FLASH_START_ADDRESS
| bootloader |
| |
+------------+
| | FLASH_START_ADDRESS + size(bootloader)
| deviceTree |
| |
+------------+
| | FLASH_START_ADDRESS + size(bootloader)
| kernel | + size(DTB)
| |
+------------+
| | FLASH_START_ADDRESS + size(bootldr)
| filesystem | + size(DTB) + size(kernel)
| |
+------------+
Note: the final value of size(bootldr) + size(DTB) + size(kernel) + size(filesystem) must be less or equal than size(FLASH).
On this microcontroller, the Flash starting address is 0x08000000.

## Slide 10
Customized Bootloader
The chosen bootloader has been forked from mcoquelin's af-boot fork. This customized fork is done in order to introduce the support for the NUCLEO-F401RE board, since the mcoquelin's one on GitHub only supports the boards based on STM32F429, STM32F469, STM32F746, STM32F769 and STM32H743 microcontrollers.
The new files are obtained by copying the existing ones and modifying the parts which differs in terms of architecture performance and hardware resources.

## Slide 11
Customized Bootloader
The bootloader is designed to start at every reset event (whether HW or SW resets), so it is located in the lowest section of the Flash memory.
Note: once the bootloader is compiled, its size can be used to determine at which address the kernel should be placed, in order to optimally use the Flash address space.
The bootloader's size is the offset from the Flash starting address. So, in the kernel configuration (see “Kconfig” section), at the "XIP Kernel Physical Location", set the address as:
FLASH_STARTING_ADDRESS + BOOTLOADER_SIZE + DTB_ADDRESS

## Slide 12
Customized Bootloader
Now, analyzing the compiled bootloader reveals its final size:
arm-none-eabi-size stm32f401re-nucleo.elf
text data bss dec hex filename
1106 0 0 1106 452 …
So, in order to set the right kernel start position, also the Device Tree Blob (flat device tree) dimension is needed.
Note: also the bootloader's Makefile should be update with the new size info and recompiled.

## Slide 13
Device Tree Blob
The DTB is the data structure used to describe the hardware of the system.
Usually, it must be generated with a proper description language and then compiled.
Finally, it must be packed with everything else in a proper image and writtent into the Flash.
But the Linux source tree provides a mean to embed the DTB directly into the kernel thanks to the file arch/arm/mach-stm32/board-dt.c: it contains the DTBs for the supported STMicroelectronics boards.

## Slide 14
Device Tree Blob
Since no board is selected (during the Kconfig step), it defaults to "NULL" and then a compiled dtb is produced.
It is not code, but read-only data. By using the "size" command on board-dt.o, the required dimension is obtained:
text data bss dec hex filename
235 0 0 235 eb arch/arm/mach- stm32/board-dt.o

## Slide 15
Device Tree Blob
But in reality, this is not something to be worried about because this piece of information is already embedded into the kernel and linked in the arch/arm/mach-stm32/Makefile.
So, only the bootloader size is needed to find the kernel starting address. So the final starting kernel address is:
0x08000000 + 0x0452 = 0x08000452
So, the kernel configuration can now be adapted accordingly.

## Slide 16
Filesystem
The filesystem is a block of memory arranged in a suitable way for the kernel to be read and understood.
It contains the executables and files related to the execution of the processes.
The chosen filesystem is CRAMFS, which support the in-place execution of uncompressed binaries.
Decompression would be too computational heavy and it would require even more RAM.
Also, CRAMFS can nicely fit in an embedded Flash memory.

## Slide 17
Kconfig: Kernel Configuration
First of all, the kernel needs to be configured before compiling it. This is done by using the tools provided with the Linux' Source Code.
The starting point is the minimal base configuration. This is obtained with "make" targeting "tinyconfig":
make ARCH=arm O=build/stm32f401re tinyconfig
Then after that, a more useful configuration is produced (using the graphical menu):
make ARCH=arm O=build/stm32f401re menuconfig

## Slide 18
Kconfig: Kernel Configuration
Note: while further specific Kconfig exist for STM32-based development boards, those boards use microcontrollers different from the STM32F401RE in clock frequency and most importantly in Flash and Sram size.
The stm32_defconfig target already exists, but it supports by default too many features which rely on the additional HW resources provided by the boards (mentioned in arch/arm/mach-stm32/board-dt.c).
It is pointless to start from this target and then remove most of the default configurations shipped with it...

## Slide 19
Kconfig: Kernel Configuration
In the graphical menu, various modification to the configuration are performed.The following functionalities have been added:
General setup
Preemption Model
Preemptible Kernel
Configure standard kernel features
Enable support for printk
System Type
STMicroelectronics STM32 family

## Slide 20
Kconfig: Kernel Configuration
Note: kernel supports STM32F429, STM32F469, STM32F746, STM32F769 and STM32H743. STM32F401 not present, so at the moment, none of the sub-selections is active
Boot options
Kernel Execute-In-Place from ROM
XIP Kernel Physical Location (0x08000452)
Executable file formats
Kernel support for flat binaries

## Slide 21
Kconfig: Kernel Configuration
Device Drivers
Character Devices
Enable TTY
Serial drivers
STMicroelectronics STM32 s-
erial port support
Support for console on STM-
32
Memory Technology Device (MTD) support

## Slide 22
Kconfig: Kernel Configuration
File systems
Miscellaneous filesystems
Compressed ROM file system support-
(cramfs)
Support CramFs image directly mapp-
ed in physical memory
The kernel needs to be executed in-place and stored in an uncompressed way in order to be RAM efficient and not pay for decompression's computational cost.

## Slide 23
Kernel Compilation
The kernel now needs to be compiled. The first concern is about the proper cross-compilation toolchain.
The compiler used is gcc-arm-linux-gnueabihf.
It targets to the ARMhf architectures (which can also take advantage of DSP instructions), uses glibc as C library (either newlibc or uClib can be used, but those are not standard).
The compiler is invoked by the Makefile (in the kernel’s root directory) with the correct flag set for CROSS_COMPILE. The resulting command is:
make ARCH=arm CROSS_COMPILE=arm-linux-gnueabihf- \
-C build/stm32f401re -j4

## Slide 24
Kernel Compilation
Note: the -jN is only for the host machine, which will dedicate 4 threads to the "make" workload.
In quite short time, the object file vmlinux.o, the executable vmlinux and the executable image xipImage are produced.
The code is compiled already with the flag -Os, thus optimizing it for size reduction.

## Slide 25
Kernel Compilation
In order to do so, the compiler exploits the ARM's Thumb Instruction set, which is a 16-bits Instruction Set.
This means that every Flash address can hold two instructions, if properly alligned during linking.
Now, after having the the executable kernel, it must be evaluated if it is suitable for the microcontroller…
But it's not!

## Slide 26
Kernel Tinyfication
The kernel's memory footprint is divided into two categories: ROM footprint and RAM footprint.
The upper limit is set by the STM32F401's Flash size and Sram size respectively.
The ROM footprint is basically composed by the .text and .rodata sections, while the RAM footprint is basically composed by the .data and .bss sections.

## Slide 27
Kernel Tinyfication
After an initial compilation (as seen in “Kernel Compilation”), the resulting kernel have been analyzed with the “size” command to evaluate the kernel's memory footprint. The result:
size vmlinux
text data bss dec hex
974288 492333 169300 1635921 18f651

## Slide 28
Kernel Tinyfication
The kernel's .text and .data sections are very large with respect to the available Flash (512kB) and Sram (96kB) respectively…
It is quite clear that Linux will not fit in the former and will not have enough of the latter…
So, after the first compilation, the aim is to reduce the total kernel size.
The first approach is to search for unused/not so useful parts of the kernel.

## Slide 29
Kernel Tinyfication
This is done by using the command nm, useful to analyze the code's symbols. The used command is:
arm-linux-gnueabi-nm --size-sort --reverse-sort \
vmlinux | less
Note: less is used only as a utility to enclose and search textually inside the stream produced by nm.

## Slide 30
Kernel Tinyfication: printk buffers
The first elements in the list are related to the added printk support. To be more precise, the buffers and ring buffers used to store temporarily the data to be sent over the console.
The kernel configuration's documentation states that the ring buffer size can be adjusted using a parameter (N), where the size is 1 << N.
This parameter can vary in the range of 12 to 17 (in this architecture). So by chosing 12, the obtained buffer size is 4kB.

## Slide 31
Kernel Tinyfication: printk buffers
So, in the graphical configuration menu:
General setup
Kernel log buffer size = 12
Another parameter related to these buffers is temporary printk buffer. It follows the same rules as the previous one, so:
General setup
Temporary per-CPU printk log buffer size =
12

## Slide 32
Kernel Tinyfication: printk buffers
After a new compilation, the result is:
size vmlinux
text data bss dec hex
974288 87341 42324 1103953 10d851
The kernel’s source tree also provides a mean to evaluate the gain. Inside the scripts directory, the useful tool bloat-o-meter is placed. It is used to evaluate the changes in the kernel.
Let’s see what it has to say...

## Slide 33
Kernel Tinyfication: printk buffers
The bloat-o-meter report:
add/remove: 0/0 grow/shrink: 0/7 up/down: 0/-270872 (-270872)
Function old new delta
printk_safe_log_store 164 156 -8
__printk_safe_flush 344 328 -16
_printk_rb_static_descs 3072 1536 -1536
__log_buf 8192 4096 -4096
_printk_rb_static_infos 22528 11264 -11264
safe_print_seq 131072 4096 -126976
nmi_print_seq 131072 4096 -126976
Total: Before=1244860, After=973988, chg -21.76%

## Slide 34
Kernel Tinyfication
As can be seen, the kernel has quite shrinked in dimension, but is still not enough…
Now, re-analyzing the symbols reveals that now the biggest portion is a global text symbol related to the Human Interface Device support (~11kB).
This subsystem is the one responsible for the management of the various input peripherals.
Well, since the this kernel is aimed to a system which only support the serial port, the HID is still needed in order to allow this kind of communication.

## Slide 35
Kernel Tinyfication
A possible solution is to reduce the complexity of this code section, but this means that the code must be modified adding architecture specific code optimizations selected by means of customized macros (in order to exclude code portions).
This proposed solution is quite complex to implement and require knowledge that is not owned by the author of this experimental kernel port.
What can be done?

## Slide 36
Kernel Tinyfication: syscalls
A different solution can be the one aiming to a different target: the system calls.
Basically, since this kernel is designed to be very simple and limited in functionalities, for sure some of the syscalls can be removed.
A list of the implemented syscalls can be obtained by composing the command (1):
arm-linux-gnueabi-nm --size-sort --reverse-sort \
vmlinux | grep "[t|T] sys_"

## Slide 37
Kernel Tinyfication
Note: in this way, only the syscalls having a strong .text section are shown.
The reason for this filtering is explained in the "Kernel Tinyfication: ptrace syscall remotion" section.
Piping the output to wc, it says that 227 syscalls are implemented (228, but one is the table of syscalls).
There are a LOT of syscalls, almost certainly some of those can be removed. But which ones?

## Slide 38
Kernel Tinyfication
For example in this specific embedded system it is not expected to have processes tracing other processes.
This means that the ptrace system call can be removed.
Following this principle, some of those are chosen.
The list of syscalls (preceeded by their size and section membership), is available on project repository (it is pointless to fill +30 slides with a list...)

## Slide 39
Kernel Tinyfication
Note: removing a syscall reduce not simply by its .text shown by the (1) command. All the nested calls are also removed and so all their .text, .rodata, .data and .bss sections. This gain may be very significant.
Note: some syscalls are present in more variants. The best practice to reduce size without losing functionalities is to keep the most complete one and removing the others.
In order to be able to manipulate these (and the next ones) changes to the kernel code during its configuration, the kernel's build toolchain is also modified.

## Slide 40
Kernel-build toolchain customization
In order to be able to conditionally select or remove a feature, for example remove a system call, a series of changes have to be applied to the kernel source tree and its building chain.
First of all, the said syscall has to be made selectable by adding a related Kconfig symbol int the init/Kconfig file (so graphically configurable by menuconfig).

## Slide 41
Kernel-build toolchain customization
The structure of these customizations, inside menuconfig, is placed under "General setup -> Configure standard kernel features" and is the following:
...
[ ] ! ! ! ALLOW DANGEROUS CUSTOMIZATIONS ! ! ! --->
[*] Enable ptrace() syscall
[*] Enable fallocate() syscall
[*] Enable time related system calls --->
[*] Enable times() syscall
[*] ...
[*] ...

## Slide 42
Kernel-build toolchain customization
This structure is organized in this way to enable/disable system calls singularly (like "Enable ptrace() syscall" or "Enable times() syscall").
The functionality group (like "Enable time related system calls") enables or disables the access to the selection.
The default of every syscall selection is "y".
The added Kconfig structure is structured in order to support menu hierarchy and is the following:

## Slide 43
Kernel-build toolchain customization
menuconfig TINY_EXPERIMENTAL
bool "! ! ! ALLOW DANGEROUS CUSTOMIZATIONS ! ! !" if EXPERT
default n
help
...
if TINY_EXPERIMENTAL
config XXX_SYSCALL
bool "Enable xxx() syscall" if TINY_EXPERIMENTAL
default y
help
...

## Slide 44
Kernel-build toolchain customization
menuconfig YYYGROUP_SYSCALLS
bool "Enable yyy related system calls"
default y
help
...
if YYYGROUP_SYSCALLS
config ZZZ_SYSCALL
bool "Enable xxx() syscall" if TINY_EXPERIMENTAL
default y
help
...

## Slide 45
Kernel-build toolchain customization
...
endif # YYYGROUP_SYSCALLS
...
endif # TINY_EXPERIMENTAL
TINY_EXPERIMENTAL is a boolean variable added to allow the selection of these custom changes on the syscalls. It acts as an enable for the customizations to the kernel.

## Slide 46
Kernel-build toolchain customization
Then, to every syscall which is intended to be made conditional is associated a unique Kconfig symbol.
This symbol will be used inside the respective source file and Makefile (which is responsible for the linkage).
Note: the latter keeps track, inside in the variable obj-y, the object files to be linked by the linker at the end of compilation.

## Slide 47
Kernel-build toolchain customization
The conditonal object inclusion is obtainted by expanding the relative label defined during configuration, now associated to a variable, after the "obj-" string.
So, if the label contains "y", the object file ends inside the obj-y list, conversely by containg "n" it ends in the "obj-n", which is ignored.

## Slide 48
Kernel Tinyfication: ptrace syscall remotion
Basically, every conditional syscall is made so by making its symbol weak and fall to the function sys_ni_syscall if no strong linkage is made on the symbol.
The sys_ni_syscall is a "parachute" syscall which will simply return ENOSYS, the error for the missing system call.

## Slide 49
Kernel Tinyfication: ptrace syscall remotion
Then, the system call is made conditional by modifying the file kernel/sys_ni.c and using the macro COND_SYSCALL(<syscall>), which is defined inside the file include/linux/linkage.h (the effective actor of the weak linkage).
The macro is placed in the file line with the a comment regarding the source of that syscall (these comments are already present for every syscall).

## Slide 50
Kernel Tinyfication: ptrace syscall remotion
Finally, the respective Makefile is modified in order to change the set of object file to include in the kernel (so, the syscall won't have a strong link to its code, but fall as just said above).
The correct Makefile is inside the directory which contains the sources file where the syscall are defined.
Note: in reality, is not always possible to remove the object file, like it will be shown shortly

## Slide 51
Kernel Tinyfication: ptrace syscall remotion
Now, in order to test if the new changes affect the system in a bad way, a test over the ptrace() syscall is performed.
The only modification is now made around ptrace() only, and a new compilation is performed leaving the PTRACE_SYSCALL symbol active, just to test if the produced kernel is the same as the one obtained in the previous step.
The previous kernel has been renamed as "vmlinux.ref" and it will be used as the reference kernel (to evaluate the successive kernels).

## Slide 52
Kernel Tinyfication: ptrace syscall remotion
This is performed around the script "new_compile.sh" (in the "Project" repository), just to automate things and avoid human errors.
It is executed with the argument "-ref", in order to compare the new kernel against "vmlinux.ref" instead of "vmlinux.old" (.old is used to track the previous kernel for step-by-step compilation comparisons).
The report around this compilation is:

## Slide 53
Kernel Tinyfication: ptrace syscall remotion
New kernel size
text data bss dec hex filename
974288 87341 42324 1103953 10d851 ...vmlinux
Bloat-o-meter gain calculation
add/remove: 0/0 grow/shrink: 0/0 up/down: 0/0 (0)
Function old new delta
Total: Before=973988, After=973988, chg +0.00%
Which means that the two kernels ("vmlinux" and "vmlinux.ref") are identical.

## Slide 54
Kernel Tinyfication: ptrace syscall remotion
Now, let's try to see what happens if the ptrace() only is removed.
In order to do so, un-check the "Enable ptrace() syscall" in menuconfig.
Then, a new compilation is performed and compared against "vmlinux.ref"
Well, some errors occurred...

## Slide 55
Kernel Tinyfication: ptrace syscall remotion
arm-linux-gnueabihf-ld: arch/arm/kernel/ptrace.o: in function `arch_ptrace':
ptrace.c:(.text+0x316): undefined reference to `ptrace_request'
arm-linux-gnueabihf-ld: kernel/fork.o: in function `mm_access':
fork.c:(.text+0x802): undefined reference to `ptrace_may_access'
arm-linux-gnueabihf-ld: kernel/fork.o: in function `copy_process':
fork.c:(.text+0x116e): undefined reference to `__ptrace_link'
arm-linux-gnueabihf-ld: kernel/exit.o: in function `release_task':
exit.c:(.text+0x298): undefined reference to `__ptrace_unlink'
arm-linux-gnueabihf-ld: kernel/exit.o: in function `wait_consider_task':
exit.c:(.text+0x83a): undefined reference to `__ptrace_unlink'
arm-linux-gnueabihf-ld: kernel/exit.o: in function `do_exit':
exit.c:(.text+0xf5e): undefined reference to `exit_ptrace'
arm-linux-gnueabihf-ld: kernel/pid.o: in function `__se_sys_pidfd_getfd':
pid.c:(.text+0x752): undefined reference to `ptrace_may_access'
arm-linux-gnueabihf-ld: kernel/nsproxy.o: in function `__se_sys_setns':
nsproxy.c:(.text+0x406): undefined reference to `ptrace_may_access'

## Slide 56
Kernel Tinyfication: ptrace syscall remotion
As can be read, this is due to the dependencies of other functions to some functions which were defined inside the ptrace.o object file, which was removed by the Makefile obj-y's default list.
In order to overcome these issues, two solutions exist:
- link ptrace.o anyway for the other syscalls
- analyze the other dependencies and search for possible simplifications (partial in-place re-write or add macros to avoid the call if possible, keeping in mind that having removed the ptrace() also removes the race conditions over kernel's data structures, related to it)

## Slide 57
Kernel Tinyfication: ptrace syscall remotion
What happens if in the Makefile is kept the ptrace.o unconditionally?
This idea relies on the fact that the compilation toolchain is enough smart to not include in the final executable the functions which not have any caller.
If done so, the compiled kernel result in:

## Slide 58
Kernel Tinyfication: ptrace syscall remotion
New kernel size
text data bss dec hex filename
973384 87349 42324 1103057 10d4d1 build/stm32f401re/vmlinux
Bloat-o-meter gain calculation
add/remove: 0/2 grow/shrink: 2/2 up/down: 86/-966 (-880)
Function old new delta
ptrace_may_access 36 120 +84
ptrace_get_syscall_info 282 284 +2
ptrace_request 1152 1150 -2
task_unlock.constprop 270 240 -30
__ptrace_may_access 80 - -80
sys_ptrace 854 - -854
Total: Before=973988, After=973108, chg -0.09%

## Slide 59
Kernel Tinyfication: ptrace syscall remotion
Now, sys_ptrace is removed, but some things have shrinked, some have grown...
But most noticeably, the other functions still hold quite some code...
Quite some questions now arise... Who calls ptrace_request?
In order to answer to this question the obtained kernel is disassembled:
arm-linux-gnueabihf-objdump -S \
build/stm32f401re/vmlinux.o | less

## Slide 60
Kernel Tinyfication: ptrace syscall remotion
Recursively, for each called function, find the caller, then iterate until a mangeable point is found. Starting from "ptrace_request", the one that is desireable to be removed, the relationships are the following:
ptrace_request’s caller: arch_ptrace
arch_ptrace’s caller: show_rcu_tasks_gp_kthreads
show_rcu_task_gp_kthreads’caller: show_rcu_gp_kthreads
show_rcu_gp_kthreads’caller: rcu_fwd_progress_check

## Slide 61
Kernel Tinyfication: ptrace syscall remotion
And there it stops: no explicit caller can be found.
The group of "*_rcu_*" has to do with the Read-Copy Update subsystem, more precisely with the forward progress check, due to threads synchronization...
It doesn't sound too easy to overcome…
With regard to ptrace_may_access, it is called by:
- mm_access
- __se_sys_pidfd_getfd
- __se_sys_setns

## Slide 62
Kernel Tinyfication: ptrace syscall remotion
What can be done?
Well, a possibility is to modify the ptrace_may_access's code by analyzing what the function should return, keeping in mind that now, no ptrace can occurr.
Unfortunately, the name of this functions is misleading: its general usage is to check whether the caller is permitted to access a target task, so not limited to ptrace case. This means that it cannot be removed...

## Slide 63
Kernel Tinyfication: ptrace syscall remotion
Now let's analyze another thing that is referred into ptrace.o: exit_ptrace.
This function is called by do_exit, which is called after one of the possible process exit scenarios. The exit_ptrace is called by the process which exits, because in case it is a tracer for a set of tracee processes, those must be detached or killed.
Now yes, in this case, since no ptrace can be executed, no process can be a tracer, and thus this code can be removed without problems.

## Slide 64
Kernel Tinyfication: ptrace syscall remotion
Now, the best practice in terms of code organization is not to modify every source file which calls the exit_ptrace, but instead keep the ptrace-related changes as little and as centralized as possible.
So, leave those functions which call it as they are and modify the exit_ptrace body by means of conditional compilation around the CONFIG_PTRACE_SYSCALL symbol.
The new exit_ptrace function looks like this:

## Slide 65
Kernel Tinyfication: ptrace syscall remotion
void exit_ptrace(struct task_struct *tracer, struct list_head *dead)
{
#ifdef CONFIG_PTRACE_SYSCALL
struct task_struct *p, *n;
list_for_each_entry_safe(p, n, &tracer->ptraced, ptrace_entry) {
if (unlikely(p->ptrace & PT_EXITKILL))
send_sig_info(SIGKILL, SEND_SIG_PRIV, p);
if (__ptrace_detach(tracer, p))
list_add(&p->ptrace_entry, dead);
}
#endif
}

## Slide 66
Kernel Tinyfication: ptrace syscall remotion
A new compilation reveals how much has been saved in terms of .text:
New kernel size
text data bss dec hex filename
973288 87349 42324 1102961 10d471 build/stm32f401re/vmlinux
Bloat-o-meter gain calculation
add/remove: 0/1 grow/shrink: 2/1 up/down: 128/-248 (-120)
Function old new delta
ptrace_request 1150 1276 +126
ptrace_resume 152 154 +2
exit_ptrace 108 2 -106
__ptrace_detach.part 142 - -142
Total: Before=973108, After=972988, chg -0.01%

## Slide 67
Kernel Tinyfication: ptrace syscall remotion
Which is still very little... But the exit_ptrace effect is visible.
Now, let's deeply analyze the ptrace_request.
Well, until now it has been considered not removable because of a chain of dependencies...
To be honest, the dependency of arch_ptrace to higher hierarchies levels is not explicitly linked to ptrace_request: the code of arch_ptrace is a "switch" statement where only one "case" has the effect of calling ptrace_request.

## Slide 68
Kernel Tinyfication: ptrace syscall remotion
If it is possible to check that the higher level functions never passes the argument which cause the ptrace_request, well, even the latter can be removed.
But something strange happened to the code: disassembling the code, it can be seen that in the object file arch_ptrace is called by show_rcu_task_kthreads, while in the executable code no function ever calls arch_ptrace explicitly...

## Slide 69
Kernel Tinyfication: ptrace syscall remotion
vmlinux.o:
0001fca0 <show_rcu_tasks_gp_kthreads>:
1fca0: f7ff bffe b.w 9c8 <arch_ptrace+0x3c>
vmlinux:
08028760 <show_rcu_tasks_gp_kthreads>:
8028760: f093 bb5a b.w 80bbe18 <show_rcu_tasks_classic_gp_kthread>
Note: this outcome is not expected. This goes beyond the author comprension (which suggests that a link is a matter of address binding, and seems that something different happened since now the extended-32bit-branch goes to a different address/label).

## Slide 70
Kernel Tinyfication: ptrace syscall remotion
Note: This is probably a BUG, because after dropping a kernel feature (preemptivity), the strange call by the RCU-related function in the object file disappeared.
The arch_ptrace is hanging by itself with no caller.
This remotion tentative is still in development stage…
Finally, compile out the syscall entry point (SYSCALL_DEFINE.(<syscall>, ...)).
In order to do so, enclose the header and its body around the test over the respective label.

## Slide 71
Kernel Tinyfication: overall syscall remotion
So, the flow is applied in a similar way to all the syscalls that can be removed. The syscalls set which will be removed is (sorted by (1)):
ptrace: tracer-tracee relationship won't be supported
times: a process' CPU time won't be track-able
settimeofday: time change not supported
gettimeofday: time access not supported
getitimer: support instead the POSIX's timer_gettime
setitimer: support instead the POSIX's timer_settime
clock_adjtime: do not support kernel clock tuning

## Slide 72
Kernel Tinyfication: overall syscall remotion
ntp_adjtime: do not support kernel clock tuning
adjtimex: do not support kernel clock tuning
clock_settime: do not support clocks
clock_gettime: do not support clocks
clock_getres: do not support clocks
clock_nanosleep: do not support clocks
utime: file last access modification won't be supported
utimes:file last access modification won't be supported
utimensat: file timestamps won't be supported
futimens: file timestamps won't be supported

## Slide 73
Kernel Tinyfication: overall syscall remotion
stime: time won't be set-able
futimesat: file descriptor timestamp won't be supported
select: support poll/ppoll instead (more file descr.s)
pselect: same reason as select
old_select: old system calls won't be supported
old_mmap: old system calls won't be supported
old_shmctl: old system calls won't be supported
old_semctl: old system calls won't be supported
old_msgctl: old system calls won't be supported
fallocate: no real appreciable performance improvement

## Slide 74
Kernel Tinyfication: overall syscall remotion
Note: the support to signals is kept as a way for processes to interact with each other.
Note: since the HW clock on-board is not persistent (external supply needed), time/time32 can be used to get the system up-time. Furthermore, having the possibility to change the HW clock using the NTP protocol is not viable since no way to contact an NTP server is provided.
So time and clocks won't be settable.

## Slide 75
Kernel Tinyfication: overall syscall remotion
Now, the same flow is applied to the other syscalls. A simple but fast and effective way to find the entry point and the syscall definition is to execute the following command at the root of the kernel source tree:
grep -rn --color=always "SYSCALL_DEFINE.(<name>" . \
| grep -v "\./build"
Once found the file, add the conditional-izing statement in sys_ni.c file at the right line where the file is cited. Then a compilation is performed and compared against the reference kernel.

## Slide 76
Kernel Tinyfication: overall syscall remotion
times:
kernel/sys_ni.c: COND_SYSCALL(times);
kernel/sys.c: #ifdef CONFIG_TIMES_SYSCALL
SYSCALL_DEFINE1(times, …) {...}
#endif
kernel/Makefile: <un-removable obj module>
Net result: Bloat-o-meter gain calculation
add/remove: 0/1 grow/shrink: 0/0 up/down: 0/-116 (-116)
Function old new delta
sys_times 116 - -116
Total: Before=973988, After=973872, chg -0.01%

## Slide 77
Kernel Tinyfication: overall syscall remotion
gettimeofday & settimeofday:
kernel/sys_ni.c: COND_SYSCALL(gettimeofday);
COND_SYSCALL(settimeofday);
kernel/time/time.c: #ifdef CONFIG_XETTIMEOFDAY_SYSCALLS
SYSCALL_DEFINE2(gettimeofday, ...) {...}
...
SYSCALL_DEFINE2(settimeofday, ...) {...}
#endif
kernel/Makefile: <un-removable obj module>
Net result: Bloat-o-meter gain calculation
add/remove: 0/2 grow/shrink: 0/0 up/down: 0/-184 (-184)
Function old new delta
sys_gettimeofday 80 - -80
sys_settimeofday 104 - -104
Total: Before=973988, After=973804, chg -0.02%

## Slide 78
Kernel Tinyfication: overall syscall remotion
Note: an error occurred while loading because the syscall clock_settime use a subroutine of settimeofday. Since it is made possible to select the syscalls independently, the do_sys_settimeofday64 must be kept outside the condition around the CONFIG_XETTIMEOFDAY_SYSCALL.
getitimer & setitimer:
Note: these two syscalls are not present if CONFIG_POSIX_TIMERS is not defined. Skipped.

## Slide 79
Kernel Tinyfication: overall syscall remotion
clock_adjtime, clock_adjtime32, adjtimex & adjtimex_time32:
kernel/sys_ni.c: COND_SYSCALL(clock_adjtime);
COND_SYSCALL(clock_adjtime32);
COND_SYSCALL(adjtimex);
COND_SYSCALL(adjtimex_time32);
kernel/time/posix-timers.c:
#ifdef CONFIG_KCLOCKTUNE_SYSCALLS
SYSCALL_DEFINE2(clock_adjtime, ...) {...}
...
SYSCALL_DEFINE2(clock_adjtime32, ...) {...}
#endif
kernel/time/time.c: #ifdef CONFIG_KCLOCKTUNE_SYSCALLS
SYSCALL_DEFINE1(adjtimex, ...) {...}
...
SYSCALL_DEFINE1(adjtimex_time32, ...) {...}
#endif
kernel/time/Makefile: <un-removable obj module>

## Slide 80
Kernel Tinyfication: overall syscall remotion
Note: the syscalls have not been removed! Seems like these functions cannot be removed...
Note: from now on, the results won't be reported for every single remotion, but a final report with everything applied will be given.

## Slide 81
Kernel Tinyfication: overall syscall remotion
clock_settime, clock_gettime, clock_getres: CONFIG_CLOCKTIME_SYSCALLS.
The definitions also exist in kernel/time/posix-stubs.c, but these can't be removed because the stubs are used as a fallback in case POSIX timers are not enabled in the kernel configuration.
Note: also in this case seems to be not possible to remove these syscalls...

## Slide 82
Kernel Tinyfication: overall syscall remotion
utime, utime32, utimes & utimes_time32:
kernel/sys_ni.c: COND_SYSCALL(utime);
COND_SYSCALL(utimes);
// already conditional
COND_SYSCALL(utime32);
// already conditional
COND_SYSCALL(utimes_time32);
fs/utimes.c: #ifdef CONFIG_UTIMEX_SYSCALLS
SYSCALL_DEFINE2(utime, ...) {...}
...
SYSCALL_DEFINE2(utimes, ...) {...}
...
// already conditional
SYSCALL_DEFINE2(utime32, ...) {...}
...
// already conditional
SYSCALL_DEFINE2(utimes_time32, ...) {...}
#endif

## Slide 83
Kernel Tinyfication: overall syscall remotion
fs/Makefile: <un-removable obj module>
Note: also in this case, the kernel haven't changed…
utimensat & utimensat_time32:
kernel/sys_ni.c: COND_SYSCALL(utimensat);
// already conditional
COND_SYSCALL(utimensat_time32);
fs/utimes.c: #ifdef CONFIG_UTIMENSAT_SYSCALLS
SYSCALL_DEFINE4(utimensat, ...) {...}
...
SYSCALLS_DEFINE4(utimensat_time32) {...}
#endif
fs/Makefile: <un-removable obj module>
Note:Total: Before=973988, After=973908, chg -0.01%

## Slide 84
Kernel Tinyfication: overall syscall remotion
futimesat & futimesat_time32:
kernel/sys_ni.c: COND_SYSCALL(futimesat);
// already conditional
COND_SYSCALL(futimesat_time32);
fs/utimes.c: #ifdef CONFIG_FUTIMESAT_SYSCALL
SYSCALL_DEFINE3(futimesat, ...) {...}
...
SYSCALL_DEFINE3(futimesat_time32, …) {...}
#endif
fs/Makefile: <un-removable obj module>
Note: no kernel size improvement...

## Slide 85
Kernel Tinyfication: overall syscall remotion
stime & stime32:
kernel/sys_ni.c: COND_SYSCALL(stime);
// already conditional
CONS_SYSCALL(stime32);
kernel/time/time.c: #ifdef CONFIG_STIME_SYSCALL
SYSCALL_DEFINE1(stime, ...) {...}
...
SYSCALL_DEFINE1(stime32, ...) {...}
#endif
kernel/time/Makefile:<un-removable obj module>
Note: no improvement...

## Slide 86
Kernel Tinyfication: overall syscall remotion
clock_nanosleep & clock_nanosleep_time32:
kernel/sys_ni.c: COND_SYSCALL(clock_nanosleep);
// already conditional
COND_SYSCALL(clock_nanosleep_time32);
kernel/time/posix-timers.c:
#ifdef CONFIG_CLOCKNANO_SYSCALL
SYSCALL_DEFINE(clock_nanosleep) {...}
...
SYSCALL_DEFINE(clock_nanosleep_time32) {...}
#endif
kernel/time/Makefile:<un-removable obj module>
Note: no improvement...

## Slide 87
Kernel Tinyfication: overall syscall remotion
old_select, select, pselect6, pselect6_time32 & pselect6_time64:
kernel/sys_ni.c: COND_SYSCALL(old_select);
COND_SYSCALL_COMPAT(old_select);
COND_SYSCALL(select);
COND_SYSCALL_COMPAT(select);
COND_SYSCALL(pselect6n);
COND_SYSCALL_COMPAT(pselect6_time64);
// already conditional
COND_SYSCALL(pselect6_time32);
// already conditional
COND_SYSCALL_COMPAT(pselect6_time32);

## Slide 88
Kernel Tinyfication: overall syscall remotion
fs/select.c: #ifdef CONFIG_XSELECT_SYSCALLS
SYSCALL_DEFINE1(old_select) {...}
SYSCALL_DEFINE6(select) {...}
SYSCALL_DEFINE6(pselect6) {...}
SYSCALL_DEFINE6(pselect6_time32) {...}
COMPAT_SYSCALL_DEFINE1(old_select) {...}
COMPAT_SYSCALL_DEFINE6(select) {...}
COMPAT_SYSCALL_DEFINE6(pselect6_time64) {...}
COMPAT_SYSCALL_DEFINE6(pselect6_time32) {...}
#endif
fs/Makefile: <un-removable obj module>
Note: Total: Before=973988, After=973654, chg -0.03%

## Slide 89
Kernel Tinyfication: overall syscall remotion
fallocate:
kernel/sys_ni.c: COND_SYSCALL(fallocate);
fs/open.c: #ifdef CONFIG_FALLOCATE_SYSCALL
SYSCALL_DEFINE4(fallocate, ...) {...}
#endif
fs/Makefile: <un-removable obj module>
Note: Total: Before=973988, After=973984, chg -0.00% (almost null gain)

## Slide 90
Kernel Tinyfication: overall syscall remotion
old_mmap, old_shmctl, old_semctl, old_msgctl:
kernel/sys_ni.c: COND_SYSCALL(old_mmap);
mm/mmap.c: #ifdef CONFIG_OLDMMAP_SYSCALL
SYSCALL_DEFINE1(old_mmap, ...) {...}
#endif
mm/nommu.c: #ifdef CONFIG_OLDMMAP_SYSCALL
SYSCALL_DEFINE1(old_mmap, ...) {...}
#endif
mm/Makefile: <un-removable obj module>
Note: Actually, old_shmctl and old_msgctl are already not present in the
final kernel due to ipc communicaiton not being supported. Same goes for
old_semctl.
Note: Total: Before=973988, After=973936, chg -0.01%

## Slide 91
Kernel Tinyfication: overall syscall remotion
Now, compiling with everything disabled produce the following result:
New kernel size
text data bss dec hex filename
972440 87349 42324 1102113 10d121 build/stm32f401re/vmlinux
Bloat-o-meter gain calculation
add/remove: 0/14 grow/shrink: 7/2 up/down: 422/-2192 (-1770)
Function old new delta
sys_ppoll 98 304 +206
ptrace_request 1152 1276 +124
ptrace_may_access 36 120 +84

## Slide 92
Kernel Tinyfication: overall syscall remotion
sys_poll 130 132 +2
split_vma 260 262 +2
ptrace_resume 152 154 +2
ptrace_get_syscall_info 282 284 +2
sys_select 2 - -2
sys_fallocate 4 - -4
task_unlock.constprop 270 240 -30
sys_old_select 32 - -32
sys_old_mmap 54 - -54
sys_utimensat 80 - -80
sys_gettimeofday 80 - -80

## Slide 93
Kernel Tinyfication: overall syscall remotion
__ptrace_may_access 80 - -80
sys_settimeofday 104 - -104
exit_ptrace 108 2 -106
kern_select 112 - -112
sys_times 116 - -116
sys_pselect6 132 - -132
__ptrace_detach.part 142 - -142
poll_select_finish 264 - -264
sys_ptrace 854 - -854
Total: Before=973988, After=972218, chg -0.18%

## Slide 94
Kernel Tinyfication: overall syscall remotion
Well... It is not that much of a saving... 1770 net bytes less... It would be really nice to completely remove the ptrace_request and almost doubling the gain that has been obtained.
To further search between the implemented syscalls which one could be removed, a list of these can be retrieved by executing the following command:
arm-linux-gnueabihf-objdump -S \
build/stm32f401re/vmlinux | \
grep "^[0-9\|a-f]\+ <.*sys_.*>:" | less

## Slide 95
Kernel Tinyfication: overall syscall remotion
Note: NOT ALL the lines are syscalls, but sure mostly are.
The syscall remotion way is quite long and it doesn't produce the hoped results.

## Slide 96
Kernel Tinyfication: obj-files compile out
Now, giving a look inside the disassembled code of the kernel, some ntp-related parts are still there, even after the ntp disabling...
What happens if the respective Makefile is modified in order to remove from the obj-y list the file?
In the case of the ptrace.o, it was not possible... Let's try it out on the ntp.o. In order to support the compile-out, new labels are introduced in the init/Kconfig:

## Slide 97
Kernel Tinyfication: obj-files compile out
menuconfig COMPILE_INFRASTRUCTURE
bool "Enable object file inclusion"
default y
help
Remove the unused but still linked object files from the kernel
to reduce memory footprint.
if COMPILE_INFRASTRUCTURE
config NTP_OBJ
bool "Keep ntp.o file in linkage list"
default y
help
Keep linking the ntp.o file
...
endif # COMPILE_INFRASTRUCTURE

## Slide 98
Kernel Tinyfication: obj-files compile out
The kernel/time/Makefile is modified by splitting the list in a fixed one and a conditionally added element as shown:
########################################################################
# OLD obj-y LIST #
########################################################################
# obj-y += timekeeping.o ntp.o clocksource.o jiffies.o timer_list.o
########################################################################
# NEW obj-y LIST #
########################################################################
obj-$(CONFIG_NTP_OBJ) += ntp.o
obj-y += timekeeping.o clocksource.o jiffies.o timer_list.o
Disabling it and recompiling, produce some errors, like the ptrace case:

## Slide 99
Kernel Tinyfication: obj-files compile out
arm-linux-gnueabihf-ld: kernel/time/timekeeping.o: in function `timekeeping_update':
timekeeping.c:(.text+0x46e): undefined reference to `ntp_clear'
arm-linux-gnueabihf-ld: timekeeping.c:(.text+0x472): undefined reference to `ntp_get_next_leap'
arm-linux-gnueabihf-ld: kernel/time/timekeeping.o: in function `accumulate_nsecs_to_secs.constprop.0':
timekeeping.c:(.text+0x72e): undefined reference to `second_overflow'
arm-linux-gnueabihf-ld: kernel/time/timekeeping.o: in function `timekeeping_advance':
timekeeping.c:(.text+0x804): undefined reference to `ntp_tick_length'
arm-linux-gnueabihf-ld: timekeeping.c:(.text+0x832): undefined reference to `ntp_tick_length'
arm-linux-gnueabihf-ld: timekeeping.c:(.text+0xa90): undefined reference to `ntp_tick_length'
arm-linux-gnueabihf-ld: kernel/time/timekeeping.o: in function `do_adjtimex':
timekeeping.c:(.text+0x200a): undefined reference to `__do_adjtimex'
arm-linux-gnueabihf-ld: timekeeping.c:(.text+0x2032): undefined reference to `ntp_get_next_leap'
arm-linux-gnueabihf-ld: kernel/time/timekeeping.o: in function `timekeeping_init':
timekeeping.c:(.init.text+0xd2): undefined reference to `ntp_init'

## Slide 100
Kernel Tinyfication: obj-files compile out
But this time, let's try to do something for these broken references. After a change, a new compilation is performed to check which references remain.
The principle of this solution is to provide a group of definintions in-place for the function bodies that have been removed with ntp.o altogether.
Of course these function bodies are enclosed around the classic conditional compilation structure with a test over the label.
The construct is added at the top of the file (because of C language matters).

## Slide 101
Kernel Tinyfication: obj-files compile out
kernel/time/timekeeping.c: undefined reference to `ntp_clear':
- ntp_clear() call can be directly defined as an empty function,
since the clearing operations are not needed.
kernel/time/timekeeping.c: undefined reference to `ntp_get_next_leap':
- the function ntp_get_next_leap() will simply return KTIME_MAX,
condition for no leapsecond pending.
kernel/time/timekeeping.c: undefined reference to `second_overflow':
- this is function will just return 0, which is the condition
where leap detection tells that no leap is present (the amount
of seconds to add or remove which have been accumulated due to
errors)

## Slide 102
Kernel Tinyfication: obj-files compile out
kernel/time/timekeeping.c: undefined reference to `ntp_tick_length':
- In this case it is quite difficult to understand what the default
value should be... A safe value to be returned can be the value
stored by default into the variable "ntpinterval". This value is
equal to NTP_INTERVAL_LENGTH << clock->shift. So, under the
hypothesys that no shift in needed, it can return the
NTP_INTERVAL_LENGTH value.
kernel/time/timekeeping.c: undefined reference to `__do_adjtimex':
- For the moment, just return that everything is ok with TIME_OK.
kernel/time/timekeeping.c: undefined reference to `ntp_init':
- An empty function (because calls ntp_clear, already empty, and since no
cmos clock is on board, the called function ntp_init_cmos_sync already
exists in the empty variant).

## Slide 103
Kernel Tinyfication: obj-files compile out
Now the linking can proceed without errors. The resulting kernel is the following:
New kernel size
text data bss dec hex filename
818620 84513 42164 945297 e6c91 build/stm32f401re/vmlinux
Bloat-o-meter gain calculation
add/remove: 2/23 grow/shrink: 1/13 up/down: 564/-2718 (-2154)
[... many lines...]
Total: Before=830844, After=828690, chg -0.26%
That's not a big change, but still appreciated...

## Slide 104
Kernel Tinyfication: un-inlining functions
But a closer look in the kernel/time/timekeeping.c file reveals that a lot of functions are inlining their code...
This means that the same code will be replicated whenever a call to it is performed. What happens if those functions are un-inlined? Let's find out…
Also in this situation, the un-inlining is made conditional with a test over a macro. In order to support this functionality, a new label is introduced in the init/Kconfig, under the option:

## Slide 105
Kernel Tinyfication: un-inlining functions
menuconfig INLINE_INFRASTRUCTURE
bool "Enable function inlining"
default y
help
Avoid the inlining of function code to reduce the overall code
size.
if INLINE_INFRASTRUCTURE
config TIMEKEEP_INLINE
bool "Keep inlining the functions inside kernel/time/timekeep.c"
default y
help
...
endif # INLINE_INFRASTRUCTURE

## Slide 106
Kernel Tinyfication: un-inlining functions
Then, for every occurrence of the functions having "inline" give two headers, one which is the original inlined, and one having "noinline" instead.
Only one between these two is selected using the label.
The same thing has to be done over the functions prototypes in the respective headers.

## Slide 107
Kernel Tinyfication: un-inlining functions
kernel/time/timekeeping_internal.h:
...
#ifdef CONFIG_TIMEKEEP_INLINE
static inline u64 clocksource_delta(u64 now, u64 last, u64 mask)
#else
static noinline u64 clocksource_delta(u64 now, u64 last, u64 mask)
#endif
{...}

## Slide 108
Kernel Tinyfication: un-inlining functions
kernel/time/ntp_internal.h:
Few functions are present and single line statements. Not modified.
kernel/time/tick-internal.h:
A large amount of function is present (31). Well, the inline can be left on the empty or return-only-statement functions. So this file is untouched.

## Slide 109
Kernel Tinyfication: un-inlining functions
kernel/time/timekeeping.c:
Here large inlined-code is present. Wrap every non-empty-body function's header around the test over the label.
There are functions with "__always_inline", so those are ignored (performance crucial for it).
First, compile without the new symbol to test that everything is still defined as it should be. Then, compile without the inlines. The result is the following:

## Slide 110
Kernel Tinyfication: un-inlining functions
New kernel size
text data bss dec hex filename
817844 84521 42132 944497 e6971 build/stm32f401re/vmlinux
Bloat-o-meter gain calculation
add/remove: 7/0 grow/shrink: 18/16 up/down: 508/-1340 (-832)
Total: Before=828690, After=827858, chg -0.10%
The reduction is not so important also in this case, but shows the potential to be applied on large scale over the whole kernel components. Of course, this concept must be applied with consciousness...

## Slide 111
Kernel Tinyfication: RCU
What can be done now to further shrink the kernel size?
Well, there is something that has been already stumbled upon: RCU.
About the rcu subsystem, the kernel provides some features to reduce the size of the internal kernel data structures and code related to it, but the support for this is not available anymore for the preemptive kernel (since 3.11 because of marginal gains in space and thus it has been preferred to drop the TINY_PREEMPT_RCU support).

## Slide 112
Kernel Tinyfication: RCU
This means that only TINY_RCU, TREE_RCU and TREE_PREEMPT_RCU kernel configurations remains.
So... What can be done practically speaking? Well, if it is possible, sacrifice the kernel's preemptivity. If the system can still ensure the soft real-time property, the non-realtime kernel can be adopted (more details in the KERNEL TINYFICATION: PREEMPT-RT section).
Now, since the preemptivity have been abandoned, TINY_RCU is already applied by default. So, for the gains, refer to the mentioned section.
Reference: https://lwn.net/Articles/541037/

## Slide 113
Kernel Tinyfication: preempt-rt
The initial kernel has been desired to be preemptible in order to provide soft real-time performance...
But is it really needed? Well, the specific application of this kernel is not defined, the author desired it to be soft real-time because he likes embedded systems and devices…
If the standard non-realtime kernel still satisfy the timing requirements, there's no need for forcing the preemption. Moreover... The premptive property has a cost: more memory usage (ROM & RAM).

## Slide 114
Kernel Tinyfication: preempt-rt
Let's now evaluate the PREEMPT_RT cost using the reference kernel (preemptive) as the model to compare against a new kernel (non-preeemptive). The result is:
New kernel size
text data bss dec hex filename
892984 85629 42260 1020873 f93c9 .../vmlinux
Bloat-o-meter gain calculation
add/remove: 92/437 grow/shrink: 180/1117 up/down: 3236/-80417 (-77181)
[... +1000 lines of functions...]
Total: Before=973988, After=896807, chg -7.92%

## Slide 115
Kernel Tinyfication: preempt-rt
Well, that's quite of a change! The .text, .data and .bss sections have all shrinked.
So, since the main aim is to first fit the target and then ensure the performance, the preemptivity property can be dropped (not the author's light-hearted decision...)

## Slide 116
Kernel Tinyfication: modules
But how about modules?
Some modules have been built in the kernel in order to support some feature and not rely on some user-space utility. In the file "modules.builtin", a list of kernel inbuilt modules is stored.
By reading its lines, what catches the attention is the psmouse module...
Well... Why would an embedded system, which is intended to only support the serial communication, support the PS2 mouse?

## Slide 117
Kernel Tinyfication: modules
This module can be removed to further reduce the kernel size.
In order to do so, disable in the graphical menu:
Device Drivers
Input device support
Generic input layer
Mice

## Slide 118
Kernel Tinyfication: modules
A new compilation reveals the gains:
New kernel size
text data bss dec hex filename
853632 84733 42244 980609 ef681 .../vmlinux
Bloat-o-meter gain calculation
add/remove: 0/275 grow/shrink: 0/4 up/down: 0/-34156 (-34156)
[... +250 lines...]
Total: Before=896807, After=862651, chg -3.81%

## Slide 119
Kernel Tinyfication: modules
Another good result.
The same thing can be applied to the keyboard, since the kernel will only communicate bidirectionally on the serial line (well, not supporting the video output makes impossible to get a feedback over the sent characters... every I/O will be on the host machine through emulated tty).
The option is located near the mice ones. The relative gain is the following:

## Slide 120
Kernel Tinyfication: modules
New kernel size
text data bss dec hex filename
845572 84597 42236 972405 ed675 .../vmlinux
Bloat-o-meter gain calculation
add/remove: 0/46 grow/shrink: 0/5 up/down: 0/-7343 (-7343)
[... +50 lines...]
Total: Before=862651, After=855308, chg -0.85%
That's a marginal improvement, but still welcomed.

## Slide 121
Kernel Tinyfication: modules
Again, as a consequence of the previous selections, the libps2 module can now be removed because no device will use a PS/2 port.
This option is near the previous two, but under the "Hardware I/O ports" section. The result is:

## Slide 122
Kernel Tinyfication: modules
New kernel size
text data bss dec hex filename
844108 84589 42236 970933 ed0b5 .../vmlinux
Bloat-o-meter gain calculation
add/remove: 0/14 grow/shrink: 0/0 up/down: 0/-1314 (-1314)
[... some lines...]
Total: Before=855308, After=853994, chg -0.15%
What else can be done? Well, regarding the modules, it would be nice to be able to drop the crc32 and zlib_inflate modules...

## Slide 123
Kernel Tinyfication: crc32
About the crc32, it cannot be removed because of other routines using it… But the implementation can be chosen. This can help reduce the memory footprint by reducing the look-up table dimension. In the graphical menu:
Library routines
CRC32/CRC32c functions
CRC32 implementation
Slice by 8 bytes
Slice by 4 bytes
Sarwate's Algorithm (one byte at a time)

## Slide 124
Kernel Tinyfication: crc32
From top to bottom are the lesser expensive and performant.
Slice by 8 B is the default.
In this particular case, having a slower but smaller implementation can be beneficial.
Now, the effect on the kernel are analyzed in the remaining cases, and the smaller is kept:

## Slide 125
Kernel Tinyfication: crc32
Slice by 4B:
New kernel size
text data bss dec hex filename
831724 84589 42236 958549 ea055 build/stm32f401re/vmlinux
Bloat-o-meter gain calculation
add/remove: 0/0 grow/shrink: 0/5 up/down: 0/-12376 (-12376)
Function old new delta
crc32_le_base 10 8 -2
crc32_body 228 142 -86
crc32table_le 8192 4096 -4096
crc32table_be 8192 4096 -4096
crc32ctable_le 8192 4096 -4096
Total: Before=853994, After=841618, chg -1.45%

## Slide 126
Kernel Tinyfication: crc32
Slice by 1B:
New kernel size
text data bss dec hex filename
822432 84589 42236 949257 e7c09 build/stm32f401re/vmlinux
Bloat-o-meter gain calculation
add/remove: 0/1 grow/shrink: 3/3 up/down: 76/-21732 (-21656)
Function old new delta
__crc32c_le_base 8 40 +32
crc32_le_base 10 34 +24
crc32_be 20 40 +20
crc32_body 228 - -228
crc32table_le 8192 1024 -7168
crc32table_be 8192 1024 -7168
crc32ctable_le 8192 1024 -7168
Total: Before=853994, After=832338, chg -2.54%

## Slide 127
Kernel Tinyfication: zlib
One of the already in-kernel packed modules is the zlib library.
It is used to uncompress (with zlib_inflate) the data on-the-fly by the CRAMFS routines, even tho the minimal filesystem to be written in the same Flash as the kernel will not be compressed (less ROM efficient, but more RAM efficient).

## Slide 128
Kernel Tinyfication: zlib
A possible solution is a similar approach seen for the syscall: rely on tests over macros and avoid the call of the zlib routines in the cramfs functions' bodies, then rely on the linker which won't link functions code without a caller.
That's not a thing that the author will do during this initial development because of the complexity of the filesystem interactions and decompression.

## Slide 129
Kernel Tinyfication: tinyconfig+customization
An interesting analysis is the one regarding the basic "tinyconfig" kernel.
Why? Its code size is the minimum provided by the original source tree: it needs 595287 B.
It is quite close to the target Flash (524288 B).
What if the printk and serial communication are dropped, but the flat binaries ad cramfs support are kept?
A new compilation reveals that:

## Slide 130
Kernel Tinyfication: tinyconfig+customization
New kernel size:
text data bss dec hex filename
645300 47373 22332 715005 ae8fd .../vmlinux
Bloat-o-meter gain calculation
add/remove: 461/1 grow/shrink: 20/2 up/down: 48305/-156 (48149)
[...]
Total: Before=595287, After=643436, chg +8.09%
Just these simple modifications require a lot of code and variables… But at least the RAM constraint is met!

## Slide 131
Kernel Tinyfication: tinyconfig+customization
Let's now try to apply all the patches explored until now and see the result compared againt the tinyconfig:
New kernel size:
text data bss dec hex filename
619164 47289 22236 688689 a8231 .../vmlinux
Bloat-o-meter gain calculation
add/remove: 469/37 grow/shrink: 45/36 up/down: 49295/-27266 (22029)
[...]
Total: Before=595287, After=617316, chg +3.70%

## Slide 132
Kernel Tinyfication: tinyconfig+customization
This step is performed just to have a feedback regarding the direction of this experimental port.
This means that the direction of this project is the right one in the sense of the common idea behind the already known concept of "bloat-hunt" in the Linux kernel community.
But still a lot of work has to be done in order to fit the kernel in a so limited SoC. If the target were one of the already supported MCUs, well of course it would have fit (that's why already supported by the kernel).

## Slide 133
Kernel Tinyfication: tinyconfig+customization
The already supported MCUs are still interesting because of the provided performance to cost parameter:
STM32H743ZI (most powerful, already suported):
core: M7
price: ~18€
performance: 1027 DMIPS/ 2.14 DMIPS/MHz (Dhrystone 2.1)
power consumption: 160 mA @ 400Mhz, Tj = 25°C, peripherals off
(~ 400 μA/MHz) (worst case: 750 mA @ higher Tj)
STM32F401RE (the project case):
core: M4
price ~8€
performance: 105 DMIPS/1.25 DMIPS/MHz (Dhrystone 2.1))
power consumption: 146 μA/MHz (peripheral off)

## Slide 134
Kernel Tinyfication: tinyconfig+customization
But why is it still interesting?
If the MCU itself can provide enough performance for the target application, a lower hardware design cost is achieved.
Compared to a MPU system, no additional FLASH, RAM chips and their relative controllers, compact PCB area to host the system, less EMC design cost because of less PCB copper lines, and so on...

## Slide 135
Applications
Well, since the result is not the hoped one, this step cannot be performed. But at least its flow can presented.
The programs to be executed in the user space will be of course simple, because of the majority of the resources already taken by the kernel.

## Slide 136
Applications
The applications will then be compiled with the same compiler as the kernel, and then linked with a customized linkerscript.
The linkerscript must be adapted in order to take into account that not having a MMU forces the programs to have absolute addresses, and so all the programs need to be linked with consciousness about the others, in order to not overlap.

## Slide 137
Init process
Packed into the filesystem, also the init program is stored.
In this very simple embedded system, with not so many services planned to be running, it is better to also have a small init.
A possible solution can be writing one from scratch, or better, adapt an already existing simple-one.
If the latter path is chosen, a possible init can be "dumb-init", released by Yelp.

## Slide 138
Init process
In fact, this init is designed for Linux containers, but since it support signal passing, it can be interesting because of simplicity.
Also this step is still not implemented, and probably will need to be a fork from the original repository.
dumb-init source: https://github.com/Yelp/dumb-init

## Slide 139
Filesystem compilation
The filesystem should be obtained by compiling a file using some tools. These tools are provided as source code in a repository.
The tools take as input a file in which the programs have been packed and then, using the proper options, produce an uncompressed cramfs archive.
Cramfs-tools source: https://github.com/npitre/cramfs-tools

## Slide 140
Flash burning
Once everything is complete, all the read-only files (bootloader, kernel and filesystem) must be packed in a single binary file, and then using a proper tool load it into the MCU's Flash.
This can be obtained by following the approach provided in the Makefile of the af-boot bootloader.
It should be modified in order to pack also the filesystem and using openocd, send it to the board.

## Slide 141
Final Considerations
Unfortunalety, this experimental port is not complete...
It is not successful because of the MCU constraints on Flash and RAM memories, so it would not be possible to load it on the board and test it in its current state…
But the chosen path is promising: the Linux mainline kernel can be further shrinked by applying some more modifications to it (still just a little part of the kernel source and its toolchain have been modified).

## Slide 142
Final Considerations
The amount of work ahead is quite large, but it is still promising.
The port project is very interesting and challenging, besides it being a way to expand the knowledge on how an OS kernel is structured and implemented.
It is quite probable that the author will still develop this project as a hobby, hoping he will get something useful, for the community.
The author
Luca Lombardini